## Slide 1: Perception and Communications for Vulnerable Road Users safety
Pierre Merdrignac
Supervisors: Fawzi Nashashibi, Evangeline Pollard, Oyunchimeg Shagdar
RITS – Robotics and Intelligent Transport System

## Slide 2: Outline
2/24
Intelligent Transport System
  Introduction
  Rits project team
  2 solutions : Automated vehicles, On-demand transport services
  Architecture for autonomous vehicles
  Vehicular communications
Perception and communication for pedestrian safety
  Vulnerable Road Users safety
  Perception of the environment
  Vehicle-to-Pedestrian (V2P) communications
Conclusion

## Slide 3: Intelligent Transport System (ITS)
3/24
Applying information and communication technologies to transport

## Slide 4: RITS: Robotics and Intelligent Transport System Ex-IMARA
Notes: The team was created by Michel Parent in 1991. At the origin, that was not a research team but a “horizontal” team at INRIA. Its objective was the coordination and the transfert of all the research done at INRIA which can be applied to the the concepts of automated road and Cybercar. Cybercars are road vehicles with fully automated driving capabilities. A fleet of such vehicles forms a managed transportation system, for passengers or goods, on a network of roads with on-demand and door-to-door capability. This concept emerged in Europe in the early 1990's and was introduced for the first time in the Netherlands in December1997 for passenger transport at Schipol airport. Since then, it has been developped under a number of European projects such as CyberCars, CyberMove, EDICT, Netmobil and CyberC3

## Slide 5: VeDeCoM institute (Véhicle Décarbonné et Communication)
Considering the whole mobility problem
Vehicle
Eco-mobility
Vehicle Electification
Connectivity and delegated driving
Shared mobility and energy
Zero emission in urban area
Uncongested safe driving in urban area
New practices, infrastructure and services
Acceptability
Regulation
Demonstrations
Convergence towards energy efficiency
  New perspectives for personal mobility in urban and periurban areas compatible with low-carbon and renewable energy.
Notes: IEED Institute created in 2012.
2 Programs : Vehicle and Eco-Mobility
3 Working groups : Vehicle electrification, Connectivity and delegated driving, Shared mobility and energy

## Slide 6
Notes: The goal of Imara is to find new mobity solutions, in order to limit congestions, pollution, lake of space in the cities, blocked situations and in order to limit injuries by offering new mobility systems which are more safe and more reliable

## Slide 8: 3 Main research topics
Robotics & ITS
Intelligent Transportation Systems
1
Modeling of large systems
Telecommunications & Networks
2
3

## Slide 9: Generic Architecture for Automated Transportation Systems
2 canonical systems:
Automated vehicles
On-demand transportation system
Both use-cases have their specificities but,
Both use the same functional architecture with some variations
Both can share specific components (functions):
Perception: ego / geo-localization, obstacle detection,…
Planning: route planning, trajectories generation and control,…
Wireless communications
Notes: SLAM Laser
SLAMMOT Stéréo
Manœuvre dépassement
Contrôle flou
Cooperative perception

## Slide 10: Generic architecture for autonomous driving

## Slide 11: Vehicular communications
IEEE 802.11p standard
  Wirelless Access in vehicular environment
  Dedicated communication frequency
  Considering mobility
  Low latency

## Slide 12: Vulnerable Road Users (VRU) safety
Challenges of protecting pedestrians
  Large variation in appearance
  Dynamic and cluttered background
  Highly irregular pedestrian motion
  Problems of occlusion
  Real-time processing required
  High performance requirement (especially for emergency maneuvers)
According to World Health Organization Report on Road safety 2013
  More the 3000 people die daily due to dangerous driving
  Half of all road traffic deaths are among pedestrians, cyclists and motorcyclists

## Slide 13: Development of a cooperative Perception and Communication System for Vulnerables Safety
Safety issues
Perception and communication
Situation assessment enhancement

## Slide 14: Perception of the environment
Raw Laser Data
Video Data
Localisation
Mapping
Detection
Classification
Tracking

## Slide 15: Perception of the environment
Segmentation and Clustering
Obstacle detection and classification
Definition of Region of Interest
  Define region on the images (multicolor rectangles)
  Projection of laser detection in camera image (red rectangles)

## Slide 16: Perception of the environment
Segmentation and Clustering
Obstacle detection and classification
Recognition based on machine learning
  HOG detectors
  Cascade classifiers
Some false alarms

## Slide 17: Perception of the environment
Multi sensor fusion
Serial Fusion
High level fusion
Low Level Fusion
Parallel Fusion

## Slide 18: Perception of the environment
Limitations of the perception
Use of V2P communications

## Slide 19: Vehicle-To-Pedestrian (V2P) Communications
Different communication types
  Vehicle-to-Vehicle (V2V)
  Vehicle-to-Infrastructure (V2I)
  Vehicle-to-Pedestrian (V2P)
Different communication media available
  3/4G
  Wi-Fi (IEEE 802.11b/g/n/p)
  Satellite
Different architectures
  Centralized communications
  Distributed communications

## Slide 20: Vehicle-To-Pedestrian (V2P) Communications
Limited efforts on V2P
Pedestrians are equipped with smartphones
  Bluetooth
  Cellular Communications
  Wi-Fi Communications
Constraints for the system
  Reliability
  Delay
  Energy consumption
Primary Choice for Safety System
  Distributed systems
  Study of Wi-Fi systems

## Slide 21: Vehicle-To-Pedestrian (V2P) Communications
Definition of requirements for VRU safety
  Minimum distance before message should be received to avoid an accident : dmin
2 scenarios to test the signal blockage from human body
  Pedestrian carries the tablet in his front close body
  Pedestrians carries the tablet in his backpack
Measurements
  GPS Accuracy
  Packet Delivery Ratio
  Packet Inter-Reception time
A vehicle periodically broadcasts its dynamics to one pedestrian
Notes: Measurement based study

## Slide 22: Vehicle-To-Pedestrian (V2P) Communications
Results
  High positioning error (≈10m)
  High communication range (≈400m)
  Effects of human body not negligible (30% more loss at 400m)
Probability of correctly informing the pedestrian at distance dmin
  3-4 consecutives packets necessary
Blockage from human body
No blockage

## Slide 23: Vehicle-To-Pedestrian (V2P) Communications
Development of an Android application to alert pedestrians
  Geographical destination area
  Messages selected at the application level
Results
  Safe (Green)
  Warning (Yellow)
  Danger (Red)

## Slide 24: Conclusion
More experiment results on: https://team.inria.fr/imara/
Thank you for your attention!