## Slide 1: An Electro-Mechanical Model of the Heart for Cardiac Image Analysis
Epidaure
Maxime Sermesant
Hervé Delingette
Nicholas Ayache
Yves Coudière
Jean-Antoine
Désidéri
Sinus

## Slide 2: Clinical motivation
Assess ventricular function parameters from medical images:
ejection fraction,
myocardium wall thickness,
local strain and stress.

## Slide 3: Previous Work
Cardiac Image Analysis
A.J. Frangi, W.J. Niessen, M.A. Viergever, Three-dimensional modeling for functional analysis of cardiac images: A review, IEEE Transactions on Medical Imaging, 2001
Biomechanical models
X. Papademetris, A.J. Sinusas, D.P. Dione, J.S. Duncan, Estimation of 3D left ventricle deformation from Echocardiography, Medical Image Analysis, 2001
W. Lin, R. Robb, A Framework for patient specific physics based simulation and interactive Visualisation of cardiac Dynamics, MICCAI'01
Key idea: to combine electrical,
mechanical and image constraints.

## Slide 4: Key Idea
Recover
Ventricular Function
Interaction with
cardiac images
(work in progress)
Build a “Beating Heart Model” that contracts under electrical excitation.
Electrical
Model
Beating Heart Model
Electro-Mechanical
coupling
Geometric Model
Volumetric Heart
Mesh
ECG

## Slide 5: Long-term goal
Build a generic heart model and a procedure to adjust its parameters to any specific patient.
INRIA Collaborative Research Action ICEMA (Images of the Cardiac Electro-Mechanical Activity)
INRIA Projects:
Epidaure
Macs
Sinus
Sosso (coordinator)
Philips Research
France

## Slide 6: Overview
Cardiac Image Interaction
Geometric Model
Beating Heart Model
  Electrical Model
  Electro-Mechanical model

## Slide 7: 4-D Ultrasound Images
ECG
Time
3-D images obtained with a rotating 2-D probe
cylindrical geometry
Images: Philips
No Real-Time 3-D images yet 4-D ultrasound sequences synchronised on ECG.

## Slide 8: Deformable Beating Heart Model
Use deformable models framework:
  External Energy = distance to the closest boundary features,
  Internal Energy = Electro-Mechanical Beating Heart model to be described now.
Image Interaction Issues:
  images of cylindrical geometry
  stiffness of volumetric models

## Slide 9: Overview
Cardiac Image Interaction
Geometric Model
Beating Heart Model
  Electrical Model
  Electro-Mechanical model

## Slide 10: Geometrical Model
Data of a canine heart from the Bioengineering Research Group, University of Auckland, New Zealand. http://www.esc.auckland.ac.nz/Groups/Bioengineering
These data include:
  1) hexahedral mesh,
  2) muscle fibre direction
  at each node.
: fibres

## Slide 11: Geometrical Model
Space-scale of electrical phenomenon much smaller than elements finer tetrahedral mesh (interpolation of position and fibre directions)
256 nodes, 180 hexahedra.
3700 nodes, 17000 tetrahedra.
Initial: hexahedral
Final: tetrahedral
: fibres

## Slide 12: Overview
Cardiac Image Interaction
Geometric Model
Beating Heart Model
  Electrical Model
  Electro-mechanical model

## Slide 13: Heart Electrical Activity
Atrial
depolarisation
Ventricular
depolarisation
Ventricular
repolarisation

## Slide 14: Electrical Model
Action potential u computation:
FitzHugh-Nagumo Reaction-Diffusion equations,
Anisotropic diffusion tensor D based on the fibre directions.
u action potential
D diffusion tensor
f ionic current
z repolarisation variable
b repolarisation rate
c repolarisation decay

## Slide 15: Electrical Model Simulation
Isotropic Diffusion Tensor
Anisotropic Diffusion Tensor
: polarised
: depolarised
Initial Conditions: wave started near the apex for these simulations.

## Slide 16: Electrical Model: simulating singularities
: polarised
: depolarised
Initial Conditions: wave started near the apex for these simulations.

## Slide 17: Overview
Cardiac Image Interaction
Geometric Model
Beating Heart Model
  Electrical Model
  Electro-Mechanical model

## Slide 18: Myocardium Properties
The myocardium is composed of muscle fibre bundles:
It is an active non-linear viscoelastic anisotropic incompressible material.

## Slide 19: Electro-Mechanical coupling
Action potential u controls the contractile element:
  u > 0 Contraction
  u < 0 Active relaxation
u also modifies stiffness k along fibre direction.

## Slide 20: Electro-Mechanical Model
This electro-mechanical coupling system is derived from nano to mesoscopic scale:
c contractile stress
 strain
k stiffness
u action potential
J. Bestel, F. Clément, M. Sorine, A Biomechanical Model of Muscle Contraction, MICCAI'01

## Slide 21: Electro-Mechanical Model
Simplified contraction stress c started by action potential u
Piecewise linear viscoelastic anisotropic material
We use a simplified model

## Slide 22: Finite Element Method
Use a linear tetrahedral element,
Linear strain tensor E from displacement P:
Stiffness matrix K computed with transverse anisotropy,
Internal Force = K.P

## Slide 23: Simplified Contraction Stress c
Applied along the fibre direction
F contraction intensity
f fibre direction
F : approximation of the coupling equation
F
t
ta
ta+tc
contraction
relaxation
At time ta:
action potential u > 0
force generation
during tc
0
u>0
u <0

## Slide 24: Numerical Integration
Solve iteratively the 2 PDEs :
1) Compute action potential u on the ventricles
Explicit integration scheme
2) Compute mechanical contraction c from action potential u
Houbolt semi-implicit integration
scheme

## Slide 25: Contraction Model
Effect of contraction stress tensor on a piecewise linear anisotropic model
: fibre directions

## Slide 26: Summary
Electrical wave propagation,
Electro-Mechanical coupling,
Interaction of the beating heart model with 4-D cardiac images (work in progress).

## Slide 27: Perspectives
Improve mechanical and coupling models,
Integrate the model on a whole cardiac sequence,
Adjust electrical and mechanical parameters to a patient dataset.